USER MANUAL

LUX LED 1519

LED MOVIMG HEAD LIGHT

(OSRAM  RGBW 4-IN-1  19*15W)

www.prolux.net.ua

Summarize	1

Safety instruction	2

Outside size picture	2

Main function	3

DMX controller function	4

Display operation instruction	6

Menu instruction	7

XLR connection instruction	8

Wiring diagram	9

Problem analysis	10

Technical specification	12

1. Summarize

- Summarize

Thank you for purchasing our LED moving head lighting. Please read these instructions carefully before begin and operate the fixtures according to these instructions to avoid any possible damages and accidents causes by misusage.

- Products introduction

This led moving head light is designed in a fashion of hydrodynamic form. It uses high power 15w,RGBW 4-IN-1 OSRAM LED, with features of long life span, low power consumption, high brightness and good color mixing effect. Each LED can independently dimmer, fading changes and so on. The built-in program includes dimmer, strobe, eotic, gradual change, fading and so on. The light uses power switch, whose weight is light and life span is long, and it performs stably with low power consumption. The rotation angle is Pan 540°, tilt 220°. It has the functions of auto reset and correction. Focusing angle varies from 8 to 52 degree. International standard DMX 512 signal is requested.

- Packing List

  - LED moving head light    1PC

  - Bracket                 1PC

  - DMX signal cable        1PC

  - Power in cable           1PC

  - The use manual          1PC

  - Warranty Card           1PC

2. Safety Information

- Safety Notes

! Inquire the skilled people before any repair;

! Always make sure disconnect from the power source before setting up, serving and moving;.

! Avoid direct eye exposure to the fixture when it is on;

- Safety instruction

● Make sure the power supply voltage are consistent with this lights，Ensure the use of voltage is in the range of the request technical parameter.

●before the installation, please check the light’s fasteners and mechanical structure have been received in good condition and appear no damage.

●This light is designed for indoor use, working temperature is lower than 50 degree.

●The fixtures maybe mounted in any position provided there is adequate room for ventilation. Make sure there are no inflammable and explosive items(ornaments) in 0.5 meters away.

●Yellow / green cabling earthling safety; no flicker when the fixture is working on.

3. Outside Size Picture

4. Main Function

- Use high quality LED lighting source, low power consumption, high brightness, stable performance and long life.

- Use the 32-bit ARM for dimming, with a 0-16666 - class of PWM output and dimming frequencies up to 1.5K Hz;

- linear dimming 0%-100%, with effect of strobe、gradual change、jumping change and so on

- DMX512 Controller，4 button set DMX ID address with LCD display

- Auto run/ sound activated/ master slave/ interconnected multi-machine control

- using switching power supply to protect the LED to work well

- Pan 540 degrees, Tilt 220 degrees, reset function

- Focusing angle varies from 8 to 52 degree

- DMX channels optional, 19CH,23CH

- Five kinds of dimming mode，Dimmer1~4。OFF for not use. Dimming smooth without flicker from Dimmer1 to Dimmer4, smoothness from weak to strong respectively.

5. DMX Control Function

23CH

| Channel | DMX Value | Function |
| --- | --- | --- |
| 1CH | 0—255 | General dimming |
| 2CH | 0—255 | Red dimming 1 |
| 3CH | 0—255 | Green dimming 1 |
| 4CH | 0—255 | Blue dimming 1 |
| 5CH | 0—255 | White dimming 1 |
| 6CH | 0—255 | Red dimming 2 |
| 7CH | 0—255 | Green dimming 2 |
| 8CH | 0—255 | Blue dimming 2 |
| 9CH | 0—255 | White dimming 2 |
| 10CH | 0—255 | Red dimming 3 |
| 11CH | 0—255 | Green dimming 3 |
| 12CH | 0—255 | Blue dimming 3 |
| 13CH | 0—255 | White dimming 3 |
| 14CH | 0—10 11—255 | Strobe off Strobe speed（1-20Hz） |
| 15CH | 0—50 51—100 101—150 151—200 201—255 | Invalid AUTO 1 AUTO 2 AUTO 3 Keep |
| 16CH | 0—255 | Automatic speed （slow-fast） |
| 17CH | 0-255 | Pan 0--540° |
| 18CH | 0-255 | Tilt 0--220° |
| 19CH | 0-255 | Pan fine 0—2.1° |
| 20CH | 0-255 | Tilt fine 0—1.0° |
| 21CH | 0-255 | X/Y speed（fast to slow） |
| 22CH | 0-255 | Zoom (zoom in - zoom out) |
| 23CH | 0-10 11-20 21-30 31-40 41-50 51-60 61-254 255-255 | Use menu to set the Dimmer Dimmer off Dimmer 1 Dimmer 2 Dimmer 3 Dimmer 4 Setted Dimmer Reset（5 seconds） |

19CH

| Channel | DMX Value | Function |
| --- | --- | --- |
| 1CH | 0—255 | General dimming |
| 2CH | 0—255 | Red dimming 1 |
| 3CH | 0—255 | Green dimming 1 |
| 4CH | 0—255 | Blue dimming 1 |
| 5CH | 0—255 | White dimming 1 |
| 6CH | 0—255 | Red dimming 2 |
| 7CH | 0—255 | Green dimming 2 |
| 8CH | 0—255 | Blue dimming 2 |
| 9CH | 0—255 | White dimming 2 |
| 10CH | 0—255 | Red dimming 3 |
| 11CH | 0—255 | Green dimming 3 |
| 12CH | 0—255 | Blue dimming 3 |
| 13CH | 0—255 | White dimming 3 |
| 14CH | 0—10 11—255 | Strobe off Strobe speed（1-20Hz） |
| 15CH | 0-255 | Pan 0--540° |
| 16CH | 0-255 | Tilt 0--220° |
| 17CH | 0-255 | X/Y speed（fast to slow） |
| 18CH | 0-255 | Zoom (zoom in - zoom out) |
| 19CH | 0-10 11-20 21-30 31-40 41-50 51-60 61-254 255-255 | Use menu to set the Dimmer Dimmer off Dimmer 1 Dimmer 2 Dimmer 3 Dimmer 4 Setted Dimmer Reset（5 seconds） |

- Display Operation Instruction

Graphic：

1: DMX512 DMX-IN XLR socket

2: DMX512 DMX-OUT XLR socket

3: AC POWER-IN socket（AC100-240V，50-60Hz）

4: FUSE：5A

5: power switch（ON/OFF）

7. Menu Instruction

1: Press [menu] or [enter] to main menu

2: Press [up] or [down] to select options

Menu instruction as follows，bilingual：Chinese (English)

| Menu | DMX Address | 001-512 |  |
| --- | --- | --- | --- |
|  | Option | X reverse | No/Yes |
|  |  | Y reverse | No/Yes |
|  |  | XXY exchange | No/Yes |
|  |  | Dimmer mode | Off，Dimmer1-4 |
|  |  | CH mode | 19CH/23CH |
|  | Display | Language | 简体中文/English |
|  |  | Lightness | 01-32 |
|  |  | Poorlight | Constant open/No operation dim/No operation off |
|  | Manual control | CH1 | 0-255 |
|  |  | CH2 | 0-255 |
|  |  | CH3 | 0-255 |
|  |  | CH4 | 0-255 |
|  |  | CH5 | 0-255 |
|  |  | CH6 | 0-255 |
|  |  | CH7 | 0-255 |
|  |  | CH8 | 0-255 |
|  |  | CH9 | 0-255 |
|  |  | CH10 | 0-255 |
|  |  | CH11 | 0-255 |
|  |  | CH12 | 0-255 |
|  |  | CH13 | 0-255 |
|  |  | CH14 | 0-255 |
|  |  | CH15 | 0-255 |
|  |  | CH16 | 0-255 |
|  |  | CH17 | 0-255 |
|  |  | CH18 | 0-255 |
|  |  | CH19 | 0-255 |
|  |  | CH20 | 0-255 |
|  |  | CH21 | 0-255 |
|  |  | CH22 | 0-255 |
|  |  | CH23 | 0-255 |
|  | Test operation | Sound | Running… |
|  |  | Auto | Running… |
|  | Resume default | Yes/No |  |
|  | Fixture reset | Yes/No |  |

When the operating state in sound activated or automatically, this machine is the master, transmit data to the outside.

8. XLR cable connecting

- XLR cable：

The standard connection way of the XRL is: one end connect to the male plug ,and the other connect to the female.

Noted：In order to avoid failures and interference signal transmission，we connect a

resistance120Ω（1/4W） at the end of the DMX connecting as below:

- The Conversion between 3pin and 5 pin XLR

If the output cable of DMX512 controller is the 5PIN, please use 1pc 5PIN to 3PIN cable.

9. Wiring diagram

- Light connecting picture:

- Problem Analysis

| Problem | Checking way |
| --- | --- |
| Can not turn on the light | Check the power source plug is in normal or not Check the switch of the lights is off or on Check the fuse if in normal |
| DMX can not control it | Check the DMX cable is connect to the lights or not Check the DMX512 controller work in normal or not Check the DMX cable is normal or not Check if the lights is in DMX mode（A001） |
| Display not bright | When connect to the electricity，did the led flash one time? If so，the power source is normal; If not，please check if the switch and the transformer has power out Check if the power input of the IC board is normal Check if the cable connect to the display loose Change the main board to see if it is normal. Chang the display |
| LED not light | When connect to the electricity，did the led flash one time? If so，the power source is normal; If not，please check if the switch and the transformer has power out Check if the power input of the IC board is normal Check if the cable connect to the display loose Change the main board to see if it is normal. |
| Some of the LED not light | LED is connect by leds in series first, then connect parallel, so please check if the leds is loose Use the multimeter to check if the led is bright or not, of not, please change the led check whether current limiting resistor is normal or not Check constant current IC is normal or not (compared with the normal IC) |
| Single color leds always bright/not bright | Check the switch of this color is normal or not Change the IC control board |

Noted：only professional persons can do as above！

- Technical Specification

- Input voltage: AC 100V-240V/47-63HZ

- Output voltage: DC24V

- Consumption: 320W

- Lamp Type: High power LED

- Lamp Spec: OSRAM RGBW 4-IN-1 LED (19pcs)

- Constant current drive: 1000mA (single color drive)

- Refresh Rate: above 600Hz

- Life Span: over 50000 hours

- Control Signal: DMX512/sound activated/auto run

- Control mode: stand alone／master and slaver

- DMX channels: 23CH/ 19CH

- Color effect: R, G, B, W, Mixing

- Function effect: Dimmer, strobe, gradual change, sound activated

- Pan 540 degree; Tilt 220 degree; Reset

- Pan fine2.1 degree; Tilt fine 1.0 degree

- Beam angle: 8º-52º

- Cooling mode: Fan cooling

- Protection rate: IP20

- Anti-electricity intension: 1.5KV

- Insulation resistance: ＞２MΩ

- Size: 320*254*398mm

- Net weight: 15 Kg

# Text boxes

Please read over this manual before operating the light

3

2

1

5

4